## Slide 1
Snooze
SnoozeBlock
Driver
SnoozeBlock
Driver
Snooze Class handles low power modes and passes a SnoozeBlock class drivers to wakeup the processor. There is only one Snooze class.
SnoozeBlock
Driver
Driver
Driver
Driver
Driver Classes do the work, such as using a timer to wake the processor. Drivers can be added or subtracted from SnoozeBlock(s) at any time.
SnoozeBlock Class connects Driver Classes to the Snooze Class. This provides the glue to the system. Can have multiple SnoozeBlocks.
Library Structure Overview:

## Slide 2
SnoozeBlock
Drivers override enable and disable hooks (virtual functions). These are called before and after sleeping or REDUCED_CPU_BLOCK.
Driver
Low Power - Timer
Driver
Digital Pin
Driver
Compare
Driver
RTC - Alarm
Driver
TSI - Touch
Driver
User Defined Driver
Detailed view of the Driver to SnoozeBlock inheritance.
Drivers:
These core driver libraries (timer,
digital, compare, alarm, touch)
can be used by any Teensy
version.
User Defined Driver - can be
any new driver that is added.
These drivers can be specific to the
chip since all kinetis processors have their own
wakeup or low power options.
SnoozeBlock:
The glue that connects the
drivers to the sleeping
operations in the Snooze
Class. Drivers inherit from the
SnoozeBlock which provides the
drivers before and after hooks (virtual functions).
These hooks run the drivers before and after sleep
modes or the REDUCED_CPU_BLOCK macro.

## Slide 3
SnoozeBlock Class 1
Driver 1,2,3,4 inherit from this SnoozeBlock
Driver 1
Driver 2
Driver 3
Driver 4
SnoozeBlock Class 3
Driver 1,2,3 inherit from this SnoozeBlock
Driver 1
Driver 2
Driver 3
SnoozeBlock Class 2
Driver 1,2 inherit from this SnoozeBlock
Driver 1
Driver 2
Snooze Class
SnoozeBlock with drivers get passed to Snooze class.
Drivers inherit from SnoozeBlocks
which get passed to the Snooze class.
Now the Snooze class can use those drivers to wakeup
the teensy sleep modes.

## Slide 4
Snooze
Block
config1
Driver Digital
Driver Alarm
Driver Touch
Snooze
Block
config2
Driver Timer
Snooze
Block
config1
Driver Timer
#include <Snooze.h>
// Load drivers
SnoozeDigital digital;
SnoozeTimer timer;
SnoozeTimer alarm;
SnoozeTimer touch;
// install drivers to SnoozeBlocks
SnoozeBlock config1(digital, alarm, touch);
SnoozeBlock config2(timer);
void setup() {
// digital pin driver configs
digital.pinMode(21, INPUT_PULLUP, RISING);//pin, mode, type
digital.pinMode(22, INPUT_PULLUP, RISING);//pin, mode, type
// low power timer driver config
timer.setTimer(5000);// milliseconds
// rtc alarm driver config
alarm.setAlarm(0, 0, 10);// hour, min, sec
// comapre driver config
compare.pinMode(11, LOW, 1.65);//pin, mode, type, threshold(v)
// tsi touch config
touch.pinMode(0, touchRead(0) + 250); // pin, threshold;
// Config1 uninstalls its drivers and installs config2 drivers.
config1 = config2;
}
void loop() {
// now config1 equals config2, only the timer driver is installed.
Snooze.deepSleep(config1);
}
SnoozeBlocks Equalities:

## Slide 5
#include <Snooze.h>
// Load drivers
SnoozeDigital digital;
SnoozeTimer timer;
// install a driver to this configuration block.
SnoozeBlock config(digital);
void setup() {
// digital pin driver configs
digital.pinMode(21, INPUT_PULLUP, RISING);//pin, mode, type
digital.pinMode(22, INPUT_PULLUP, RISING);//pin, mode, type
// low power timer driver config
timer.setTimer(5000);// milliseconds
// "config" SnoozeBlock only has the digital driver installed,
// so we can install the timer driver like this also.
config += timer;
}
void loop() {
// now config has the digital pin and timer drivers for wakeup.
Snooze.deepSleep(config);
}
Snooze
Block
config
Driver Digital
Driver Timer
Adding a Driver to a SnoozeBlock:
Snooze
Block
config
Driver Digital
Driver Timer

## Slide 6
#include <Snooze.h>
// Load drivers
SnoozeDigital digital;
SnoozeTimer timer;
// install two drivers to this configuration block.
SnoozeBlock config(digital, timer);
void setup() {
// digital pin driver configs
digital.pinMode(21, INPUT_PULLUP, RISING);//pin, mode, type
digital.pinMode(22, INPUT_PULLUP, RISING);//pin, mode, type
// low power timer driver config
timer.setTimer(5000);// milliseconds
// SnoozeBlock "config” has both digital and timer drivers installed,
// we can subtract the timer driver like this.
config -= timer;
}
void loop() {
// now config only has the digital pin driver for wakeup.
Snooze.deepSleep(config);
}
Driver Timer
Snooze
Block
config
Driver Digital
Driver Timer
Snooze
Block
config
Driver Digital
Subtract Driver to a SnoozeBlock:

## Slide 7: REDUCED_CPU_BLOCK - Macro
Runs code inside the brackets at 2MHz.
Passes a SnoozeBlock with drivers to reconfigure modules to work at this reduced speed like the Serial ports.
Since hardware modules in Teensydunio are tied to F_CPU, F_BUS or F_MEM the modules have to be reconfigured for this reduced speed or they probably won’t work.
#include <Snooze.h>
// this basic example uses no drivers but a
// SnoozeBlockneeds to be passed to it anyways so
// we define a dummy SnoozeBlock with no drivers
// installed.
SnoozeBlock dummyConfig;
#define LED 13
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
// code inside this macro will run at 2 MHz.
// code outside will run at whatever F_CPU you
// compiled at.
REDUCED_CPU_BLOCK(dummyConfig) {
while (1) {
digitalWrite(LED, !digitalRead(LED));
// functions like delay have to be
// rewritten for cpu running at lower
//speed than it was compiled for.
delay_lp(100);
}
}
}